## Slide 1: PCME STACK 710 Opacity Measurement System
Roberto Lopez-Garcia

## Slide 2: PCME STACK710 Overview
0 - 20 - 40 - 60 - 80 - 100% Opacity
0 - 01 - 02 - 03 - 04 - 05 Ringelmann (visual)
Opacity 100% = (1 – Received Signal/Transmitted signal)
TRANSMITTER
RECEIVER

## Slide 3: Stack 710 can also be used for Dust Monitoring
Provides representative dust measurement across large stacks
Optical Density (extinction) linearises exponential relationship between dust and received light
Extinction = -Log10 (Ʈ)
Extinction = -acl/2.303
Where: n = Concentration of Pollutant
a = Attenuation Coefficient
l = Pathlength
Optical Pathlenght

## Slide 4: PCME STACK 710 Compliance
Meets or exceeds US OPACITY Standards
  US EPA requirements for 40CFR60 Sections 13, 17 and App. B PS-1.
  Meets or exceeds US EPA requirements for proposed 40CFR60 App. F procedure 3.
  Meets or exceeds ASTM Standard D6216.
  Certified to QAL1, EN15267-3, 0-15mg/m3 @5m pathlength
* Some limitations (Pathlength)

## Slide 5: STACK 710 Operation
Source LED
Flood LED
Diffusion Filter
Mirror
Beam Splitter
Retroreflector
Zero Point Reflector
Span Filter
Detectors
Source and Flood LED off – Measures the electronic zero of the detectors and automatically compensates.
Flood LED on – Determines any gain difference between the measurement and reference detectors and automatically compensates.
Zero Offset Mode

## Slide 6: STACK 710 Operation
Source LED on – The transmitted light intensity is measured by the reference detector, while the reflected light intensity is measured by the measurement detector. Opacity is calculated from the ratio of these.
Measuring Mode

## Slide 7: Reliable Automatic Calibration for High QA
Internal activation or External trigger of check cycles
  Contact closure
  Modbus
System zero calibration
  Corrects for drift
  Corrects for dust accumulation on lens
  Limited to 4% correction
System span calibration
  Verifies upscale operation
The Zero Point Reflector
A Span Filter (typically 25%)

## Slide 8: PCME STACK 710 – Key Benefits
The PCME STACK 710 is a continuous, cross stack, double pass transmissometer.
Easy maintenance and servicing
Ease of use with user interface at both transceiver and remote control unit
No continuously moving parts – high reliability
Patented LED technology and retro-reflector design for high accuracy and lower dust measurement than other Transmissometers
Compliant with all International Opacity standards
Shutters + Alignment
Purge Inlet

## Slide 9: PCME STACK 710 - Patented Retro-reflector
  Eliminates temperature drift found in traditional plastic retro-reflectors
    Can lead to over reporting of emissions
  Added Benefits
    Longer path lengths
      10m now available
    Better signal to noise
      Lower detection limits
Notes: 9

## Slide 10: Stack 710 is a great Product for Transmissometer Applications
Large stack /high dust (EP or no controls)
  Fossil Fuel Boilers and Power Plant
  Sinter plant (steel)
  Cement Kilns
Process conditions
  Opacity 0- 10% and 0-100%
  Dust : 10 – 500mg/m3
  1 – 10m stack diameter
  Non condensing flue gas
Strong performance versus major competitors
  Durag: DR-290
  Sick: Dust HunterT-200
  TeledyneML : Light Hawk

## Slide 11
Thank You